## Slide 1: UVA Brainhack!
===== Week 2 =====
6/6/2025

## Slide 2: Agenda
Rivanna
MR crash course
Formal intro to python (?)
Hacking

## Slide 3: Rivanna
High-Performance Computing @UVA
www.rc.virginia.edu
Outsourcing computations to remote servers
Everyone has been added to morrislab!

## Slide 4: OnDemand
** Must be connected to UVA network **

## Slide 5: MR Crash Course
Basics of image construction

## Slide 6: What is MRI?
Magnetic Resonance Imaging
(aka Nuclear Magnetic Resonance)

## Slide 7: What is MRI?
Magnetic Resonance Imaging
(aka Nuclear Magnetic Resonance)
Using electromagnetism to perturb atomic nuclei and record how they respond to interference

## Slide 8: MR physics
Caveat Emptor!
The following discussion will include:
  Classical mechanical descriptions of quantum phenomena
  Vector algebra (sort of)
  Point particle representations
Notes: Word to the wise
In the following discussion of MR Physics, I will be describing quantum phenomena in the language of classical mechanics. This is an approximation of the truth -- for 90 % of day-to-day MRI, the classical description is sufficient.
Ultimately, these phenomena are best understood through the lens of quantum mechanics.
Vector algebra instead of density notation
Point particles as opposed to wave functions

## Slide 9: MR physics
“Nuclear” -- atomic nuclei with special properties:
  Non-zero spin
    Intrinsic angular momentum
  Large “gyromagnetic ratio”
    Generates a strong magnetic dipole moment
    High charge-to-mass ratio
  Abundant
    ~1019 /mm
Notes: spin is an intrinsic form of angular momentum carried by elementary particles, composite particles (hadrons), and atomic nuclei
All elementary particles of a given kind have the same magnitude of spin angular momentum, which is indicated by assigning the particle a spin quantum number.

## Slide 10: MR physics
“Nuclear” -- atomic nuclei with special properties:
  Non-zero spin
    Intrinsic angular momentum
  Large “gyromagnetic ratio”
    Generates a strong magnetic dipole moment
    High charge-to-mass ratio
  Abundant
    ~1019 /mm
Notes: Hydrogen comprises 62% of the human body by number of atoms (10% by mass)

## Slide 11: MR physics
“Magnetic”
Notes: A bunch of tiny magnets

## Slide 12: MR physics
“Magnetic”
  Spin system
Outside
Inside
Notes: A bunch of tiny magnets

## Slide 13: MR physics
“Magnetic”
  Spin system
  Classical Mechanical View: magnetic moments align with applied external field
Outside
Inside
Notes: A bunch of tiny magnets

## Slide 14: MR physics

## Slide 15: MR physics

## Slide 16: MR physics

## Slide 17: MR physics
Aligned with B0 and precessing at the same rate
B0
42.58 MHz/T
“Larmour Frequency”

## Slide 18: MR physics
… But they’re out of phase!
Aligned with B0 and precessing at the same rate

## Slide 19: MR physics
B0

## Slide 20: MR physics
Net magnetization vector for the spin system
(vector algebra)
Out of phase = transverse components sum to zero!

## Slide 21: MR physics
NO SIGNAL!
Net magnetization vector for the spin system
(vector algebra)
Out of phase = transverse components sum to zero!
We are left with a static longitudinal component (no flux)

## Slide 22: MR physics
B0
LONGITUDINAL
TRANSVERSE

## Slide 23: MR physics
B0
B0
LONGITUDINAL
TRANSVERSE

## Slide 24: MR Physics
42.58MHz
“Resonance”
Notes: Technically broad-band RF to capture band around Larmour frequency

## Slide 25: MR Physics
42.58MHz
Inversion and recovery
LONGITUDINAL
TRANSVERSE
Notes: Technically broad-band RF to capture band around Larmour frequency

## Slide 26: MR Physics
Inversion and recovery
Laboratory frame
Rotating frame
Notes: Technically broad-band RF to capture band around Larmour frequency

## Slide 27: MR Physics
Inversion and recovery
Notes: Technically broad-band RF to capture band around Larmour frequency

## Slide 28: Contrast Weighting

## Slide 29: Contrast Weighting
Inversion and recovery
LONGITUDINAL
TRANSVERSE
T1 = longitudinal recovery rate
T2 = transverse decay rate
Notes: Technically broad-band RF to capture band around Larmour frequency

## Slide 30: Structural MRI
T1-weighted
Notes: This is an example T1w image, which optimizes the contrast between fatty tissue and water, with other tissue types falling somewhere in-between. These are not BOLD-sensitive (aka ‘functional’). Rather, these are static structural images.
Macrostructure (if that wasn’t obvious)

## Slide 31: Structural MRI
Image generation (finally)
Gradients are the key!
Slower precession
Faster precession
z
Notes: Draw it out

## Slide 32: YouTube

## Slide 33: Structural MRI
Image generation (finally)
Complex signal decomposition: Fourier transform
Notes: Draw it out

## Slide 34: K Space

## Slide 35: K Space

## Slide 36: BOLD fMRI
The BOLD effect
Neurons need O2 for aerobic metabolism (main source of ATP)
When action potential occurs, calcium signalling leads to downstream hemodylation, causing an influx of diamagnetic hemoglobin (Hb)

## Slide 37: BOLD fMRI
Hb

## Slide 38: BOLD fMRI
Hb  dHb

## Slide 39: BOLD fMRI
The BOLD effect

## Slide 40: BOLD fMRI
Task-based vs. resting-state paradigms
Task-based = evoking HDR
  Expect to see change in BOLD signal at specific location / cluster of voxels

## Slide 41: BOLD fMRI
GLM
https://mriquestions.com/general-linear-model.html
Notes: Each voxel has its own timeseries

## Slide 42: BOLD fMRI
GLM
https://mriquestions.com/general-linear-model.html
z-map

## Slide 43: BOLD fMRI
Resting-state fMRI

## Slide 44
Sejnowski, Churchland and Movshon, 2014, Nature Neuroscience
Hi-res
Low-res
BOLD fMRI
Notes: Ours is a blunt instrument
Not able to capture micro-scale phenomena

## Slide 45: Processing Pipeline

## Slide 46: Diffusion Imaging
Van Horn, J. D. (2023)
Notes: Water Diffusion:
  Water molecules undergo random, thermally-driven motion, known as Brownian motion. This diffusion is influenced by the microstructural environment.
  In free water, diffusion is unrestricted. In biological tissues, barriers like cell membranes, myelin sheaths, and organelles hinder diffusion, making it anisotropic (directionally dependent).
Sensitivity to Diffusion:
  DW-MRI encodes the movement of water molecules into the MRI signal using magnetic field gradients. This encoding allows the detection of microscopic variations in diffusion that provide insights into tissue structure and pathology.
2. The DW-MRI Pulse Sequence
DW-MRI uses a modified spin-echo sequence with added diffusion-sensitizing gradients. The typical sequence involves the following components:
a. Standard Spin-Echo Sequence
90° RF Pulse:
  Excites the spins in the tissue, tipping them into the transverse plane.
180° RF Pulse:
  Refocuses the spins, forming a spin echo to correct for inhomogeneities in the static magnetic field (B0B_0B0​).
b. Diffusion Gradients
To make the sequence sensitive to diffusion, two additional gradients are applied symmetrically around the 180° RF pulse:
First Gradient (Dephasing):
  A magnetic field gradient is applied to dephase the spins based on their position in space. Spins in moving water molecules are now phase-shifted according to their displacement.
Second Gradient (Rephasing):
  Another magnetic gradient, with the same amplitude and duration as the first, is applied after the 180° RF pulse. If a water molecule has not moved, its phase shift is reversed, and the spin rephases. However, if the water molecule has moved, it will not completely rephase, leading to signal attenuation.
3. Key Parameters in DW-MRI
b-Value:
  A measure of the strength and timing of the diffusion gradients, expressed in s/mm². It determines the sensitivity of the sequence to diffusion.
  Higher bbb-values increase sensitivity to diffusion but also lead to lower signal-to-noise ratios (SNR).
  Typical bbb-values are:
    Low ( 0s/mm2~0 s/mm² 0s/mm2): No diffusion weighting.
    Intermediate ( 500–1000s/mm2~500–1000 s/mm² 500–1000s/mm2): General diffusion imaging.
    High ( 2000+s/mm2~2000+ s/mm² 2000+s/mm2): Characterizing restricted diffusion (e.g., in tightly packed tumor cells).
Echo Time (TE):
  The time between the 90° RF pulse and the peak of the spin echo. Longer TE values allow for more diffusion sensitivity but may reduce SNR.
Repetition Time (TR):
  The time between successive excitations. TR is typically set long enough to allow full longitudinal relaxation and avoid T1 weighting.
4. Signal Attenuation in DW-MRI
The MRI signal in a diffusion-weighted image is attenuated according to the Stejskal-Tanner equation:
S=S0e−bDS = S_0 e^{-bD}S=S0​e−bD
SSS: Signal intensity in the diffusion-weighted image.
S0S_0S0​: Signal intensity without diffusion weighting (b=0b = 0b=0).
bbb: Diffusion weighting factor (dependent on gradient strength, duration, and spacing).
DDD: Apparent diffusion coefficient (ADC), a measure of the diffusion rate.
5. Data Representation and Analysis
a. Apparent Diffusion Coefficient (ADC) Maps
ADC maps are calculated by acquiring images with different bbb-values and fitting the Stejskal-Tanner equation to estimate the diffusion coefficient for each voxel.
Bright regions on ADC maps indicate fast diffusion (e.g., free water).
Dark regions on ADC maps indicate restricted diffusion (e.g., cytotoxic edema in stroke).
b. Diffusion Tensor Imaging (DTI)
DTI is an extension of DW-MRI that models diffusion as a tensor, capturing the directionality (anisotropy) of water diffusion.
DTI requires diffusion measurements in multiple directions (typically >6).
Outputs include:
  Fractional Anisotropy (FA): A measure of the directionality of diffusion.
  Mean Diffusivity (MD): The average diffusion rate.
  Principal Eigenvectors: Used to map white matter tracts.

## Slide 47: Diffusion Imaging
Tracking water diffusion (along axons)
Rosenbloom et al., 2004
Notes: Water Diffusion:
  Water molecules undergo random, thermally-driven motion, known as Brownian motion. This diffusion is influenced by the microstructural environment.
  In free water, diffusion is unrestricted. In biological tissues, barriers like cell membranes, myelin sheaths, and organelles hinder diffusion, making it anisotropic (directionally dependent).
Sensitivity to Diffusion:
  DW-MRI encodes the movement of water molecules into the MRI signal using magnetic field gradients. This encoding allows the detection of microscopic variations in diffusion that provide insights into tissue structure and pathology.
2. The DW-MRI Pulse Sequence
DW-MRI uses a modified spin-echo sequence with added diffusion-sensitizing gradients. The typical sequence involves the following components:
a. Standard Spin-Echo Sequence
90° RF Pulse:
  Excites the spins in the tissue, tipping them into the transverse plane.
180° RF Pulse:
  Refocuses the spins, forming a spin echo to correct for inhomogeneities in the static magnetic field (B0B_0B0​).
b. Diffusion Gradients
To make the sequence sensitive to diffusion, two additional gradients are applied symmetrically around the 180° RF pulse:
First Gradient (Dephasing):
  A magnetic field gradient is applied to dephase the spins based on their position in space. Spins in moving water molecules are now phase-shifted according to their displacement.
Second Gradient (Rephasing):
  Another magnetic gradient, with the same amplitude and duration as the first, is applied after the 180° RF pulse. If a water molecule has not moved, its phase shift is reversed, and the spin rephases. However, if the water molecule has moved, it will not completely rephase, leading to signal attenuation.
3. Key Parameters in DW-MRI
b-Value:
  A measure of the strength and timing of the diffusion gradients, expressed in s/mm². It determines the sensitivity of the sequence to diffusion.
  Higher bbb-values increase sensitivity to diffusion but also lead to lower signal-to-noise ratios (SNR).
  Typical bbb-values are:
    Low ( 0s/mm2~0 s/mm² 0s/mm2): No diffusion weighting.
    Intermediate ( 500–1000s/mm2~500–1000 s/mm² 500–1000s/mm2): General diffusion imaging.
    High ( 2000+s/mm2~2000+ s/mm² 2000+s/mm2): Characterizing restricted diffusion (e.g., in tightly packed tumor cells).
Echo Time (TE):
  The time between the 90° RF pulse and the peak of the spin echo. Longer TE values allow for more diffusion sensitivity but may reduce SNR.
Repetition Time (TR):
  The time between successive excitations. TR is typically set long enough to allow full longitudinal relaxation and avoid T1 weighting.
4. Signal Attenuation in DW-MRI
The MRI signal in a diffusion-weighted image is attenuated according to the Stejskal-Tanner equation:
S=S0e−bDS = S_0 e^{-bD}S=S0​e−bD
SSS: Signal intensity in the diffusion-weighted image.
S0S_0S0​: Signal intensity without diffusion weighting (b=0b = 0b=0).
bbb: Diffusion weighting factor (dependent on gradient strength, duration, and spacing).
DDD: Apparent diffusion coefficient (ADC), a measure of the diffusion rate.
5. Data Representation and Analysis
a. Apparent Diffusion Coefficient (ADC) Maps
ADC maps are calculated by acquiring images with different bbb-values and fitting the Stejskal-Tanner equation to estimate the diffusion coefficient for each voxel.
Bright regions on ADC maps indicate fast diffusion (e.g., free water).
Dark regions on ADC maps indicate restricted diffusion (e.g., cytotoxic edema in stroke).
b. Diffusion Tensor Imaging (DTI)
DTI is an extension of DW-MRI that models diffusion as a tensor, capturing the directionality (anisotropy) of water diffusion.
DTI requires diffusion measurements in multiple directions (typically >6).
Outputs include:
  Fractional Anisotropy (FA): A measure of the directionality of diffusion.
  Mean Diffusivity (MD): The average diffusion rate.
  Principal Eigenvectors: Used to map white matter tracts.

## Slide 48: Diffusion Imaging
https://www.radiologycafe.com/frcr-physics-notes/mr-imaging/diffusion-weighted-imaging/
Apparent diffusion coefficient (ADC)
Notes: Water Diffusion:
  Water molecules undergo random, thermally-driven motion, known as Brownian motion. This diffusion is influenced by the microstructural environment.
  In free water, diffusion is unrestricted. In biological tissues, barriers like cell membranes, myelin sheaths, and organelles hinder diffusion, making it anisotropic (directionally dependent).
Sensitivity to Diffusion:
  DW-MRI encodes the movement of water molecules into the MRI signal using magnetic field gradients. This encoding allows the detection of microscopic variations in diffusion that provide insights into tissue structure and pathology.
2. The DW-MRI Pulse Sequence
DW-MRI uses a modified spin-echo sequence with added diffusion-sensitizing gradients. The typical sequence involves the following components:
a. Standard Spin-Echo Sequence
90° RF Pulse:
  Excites the spins in the tissue, tipping them into the transverse plane.
180° RF Pulse:
  Refocuses the spins, forming a spin echo to correct for inhomogeneities in the static magnetic field (B0B_0B0​).
b. Diffusion Gradients
To make the sequence sensitive to diffusion, two additional gradients are applied symmetrically around the 180° RF pulse:
First Gradient (Dephasing):
  A magnetic field gradient is applied to dephase the spins based on their position in space. Spins in moving water molecules are now phase-shifted according to their displacement.
Second Gradient (Rephasing):
  Another magnetic gradient, with the same amplitude and duration as the first, is applied after the 180° RF pulse. If a water molecule has not moved, its phase shift is reversed, and the spin rephases. However, if the water molecule has moved, it will not completely rephase, leading to signal attenuation.
3. Key Parameters in DW-MRI
b-Value:
  A measure of the strength and timing of the diffusion gradients, expressed in s/mm². It determines the sensitivity of the sequence to diffusion.
  Higher bbb-values increase sensitivity to diffusion but also lead to lower signal-to-noise ratios (SNR).
  Typical bbb-values are:
    Low ( 0s/mm2~0 s/mm² 0s/mm2): No diffusion weighting.
    Intermediate ( 500–1000s/mm2~500–1000 s/mm² 500–1000s/mm2): General diffusion imaging.
    High ( 2000+s/mm2~2000+ s/mm² 2000+s/mm2): Characterizing restricted diffusion (e.g., in tightly packed tumor cells).
Echo Time (TE):
  The time between the 90° RF pulse and the peak of the spin echo. Longer TE values allow for more diffusion sensitivity but may reduce SNR.
Repetition Time (TR):
  The time between successive excitations. TR is typically set long enough to allow full longitudinal relaxation and avoid T1 weighting.
4. Signal Attenuation in DW-MRI
The MRI signal in a diffusion-weighted image is attenuated according to the Stejskal-Tanner equation:
S=S0e−bDS = S_0 e^{-bD}S=S0​e−bD
SSS: Signal intensity in the diffusion-weighted image.
S0S_0S0​: Signal intensity without diffusion weighting (b=0b = 0b=0).
bbb: Diffusion weighting factor (dependent on gradient strength, duration, and spacing).
DDD: Apparent diffusion coefficient (ADC), a measure of the diffusion rate.
5. Data Representation and Analysis
a. Apparent Diffusion Coefficient (ADC) Maps
ADC maps are calculated by acquiring images with different bbb-values and fitting the Stejskal-Tanner equation to estimate the diffusion coefficient for each voxel.
Bright regions on ADC maps indicate fast diffusion (e.g., free water).
Dark regions on ADC maps indicate restricted diffusion (e.g., cytotoxic edema in stroke).
b. Diffusion Tensor Imaging (DTI)
DTI is an extension of DW-MRI that models diffusion as a tensor, capturing the directionality (anisotropy) of water diffusion.
DTI requires diffusion measurements in multiple directions (typically >6).
Outputs include:
  Fractional Anisotropy (FA): A measure of the directionality of diffusion.
  Mean Diffusivity (MD): The average diffusion rate.
  Principal Eigenvectors: Used to map white matter tracts.

## Slide 49: Diffusion Imaging
Phase tagging
Notes: Phase tagging in diffusion-weighted imaging (DWI) refers to a method used to encode diffusion information into the phase of the MRI signal. Unlike conventional DWI, where diffusion effects are primarily encoded in the signal amplitude (magnitude), phase tagging leverages phase shifts induced by the motion of spins in the presence of diffusion gradients. This approach can provide detailed information about diffusion and flow, with applications in imaging complex tissue structures or assessing flow dynamics.
Water Diffusion:
  Water molecules undergo random, thermally-driven motion, known as Brownian motion. This diffusion is influenced by the microstructural environment.
  In free water, diffusion is unrestricted. In biological tissues, barriers like cell membranes, myelin sheaths, and organelles hinder diffusion, making it anisotropic (directionally dependent).
Sensitivity to Diffusion:
  DW-MRI encodes the movement of water molecules into the MRI signal using magnetic field gradients. This encoding allows the detection of microscopic variations in diffusion that provide insights into tissue structure and pathology.
2. The DW-MRI Pulse Sequence
DW-MRI uses a modified spin-echo sequence with added diffusion-sensitizing gradients. The typical sequence involves the following components:
a. Standard Spin-Echo Sequence
90° RF Pulse:
  Excites the spins in the tissue, tipping them into the transverse plane.
180° RF Pulse:
  Refocuses the spins, forming a spin echo to correct for inhomogeneities in the static magnetic field (B0B_0B0​).
b. Diffusion Gradients
To make the sequence sensitive to diffusion, two additional gradients are applied symmetrically around the 180° RF pulse:
First Gradient (Dephasing):
  A magnetic field gradient is applied to dephase the spins based on their position in space. Spins in moving water molecules are now phase-shifted according to their displacement.
Second Gradient (Rephasing):
  Another magnetic gradient, with the same amplitude and duration as the first, is applied after the 180° RF pulse. If a water molecule has not moved, its phase shift is reversed, and the spin rephases. However, if the water molecule has moved, it will not completely rephase, leading to signal attenuation.
3. Key Parameters in DW-MRI
b-Value:
  A measure of the strength and timing of the diffusion gradients, expressed in s/mm². It determines the sensitivity of the sequence to diffusion.
  Higher bbb-values increase sensitivity to diffusion but also lead to lower signal-to-noise ratios (SNR).
  Typical bbb-values are:
    Low ( 0s/mm2~0 s/mm² 0s/mm2): No diffusion weighting.
    Intermediate ( 500–1000s/mm2~500–1000 s/mm² 500–1000s/mm2): General diffusion imaging.
    High ( 2000+s/mm2~2000+ s/mm² 2000+s/mm2): Characterizing restricted diffusion (e.g., in tightly packed tumor cells).
Echo Time (TE):
  The time between the 90° RF pulse and the peak of the spin echo. Longer TE values allow for more diffusion sensitivity but may reduce SNR.
Repetition Time (TR):
  The time between successive excitations. TR is typically set long enough to allow full longitudinal relaxation and avoid T1 weighting.
4. Signal Attenuation in DW-MRI
The MRI signal in a diffusion-weighted image is attenuated according to the Stejskal-Tanner equation:
S=S0e−bDS = S_0 e^{-bD}S=S0​e−bD
SSS: Signal intensity in the diffusion-weighted image.
S0S_0S0​: Signal intensity without diffusion weighting (b=0b = 0b=0).
bbb: Diffusion weighting factor (dependent on gradient strength, duration, and spacing).
DDD: Apparent diffusion coefficient (ADC), a measure of the diffusion rate.
5. Data Representation and Analysis
a. Apparent Diffusion Coefficient (ADC) Maps
ADC maps are calculated by acquiring images with different bbb-values and fitting the Stejskal-Tanner equation to estimate the diffusion coefficient for each voxel.
Bright regions on ADC maps indicate fast diffusion (e.g., free water).
Dark regions on ADC maps indicate restricted diffusion (e.g., cytotoxic edema in stroke).
b. Diffusion Tensor Imaging (DTI)
DTI is an extension of DW-MRI that models diffusion as a tensor, capturing the directionality (anisotropy) of water diffusion.
DTI requires diffusion measurements in multiple directions (typically >6).
Outputs include:
  Fractional Anisotropy (FA): A measure of the directionality of diffusion.
  Mean Diffusivity (MD): The average diffusion rate.
  Principal Eigenvectors: Used to map white matter tracts.

## Slide 50: Diffusion Imaging
https://mriquestions.com
Skyberg et al., 2023
Notes: Phase tagging